Lab:  Speed of a Toy Car						Names ___________________________

Date _________________							_____________________Pd ___

Background:  How long does it take a car to move 2 meters?  We all have a good idea that if it takes a smaller period of time to move 2 meters, the car must be moving faster.  But how do we measure the speed of a toy car.  In your own car, it is easy because engineers have designed a speedometer that automatically tells you how fast your car is moving.

A common unit for speed is miles per hour.  From this it is easy to figure out the formula that we have to use to calculate the speed of a toy car.

Miles is a unit to measure distance.  Hour is a unit to measure time.   And the word PER stands for division.

So, if Miles Per Hour = Miles / Hour we can replace miles with distance and hour with time and we get the following formula:

Notice that the speed is abbreviated with a V because it is associated with velocity.

In this lab, you are going to determine the speed of a toy car.

Materials:  	Toy Car	Tape		Stopwatch		Meter Stick

Predict: If you record the time it takes for the car to move 1 meter, then record the time it takes to move 3 meters, will there be a difference in the speed of the car between the two runs? Explain your prediction:

Procedures:

- Using piece of tape, mark off the following locations on the floor:  0 meters, 1 meter, 2 meters, 3 meters.

- Place the car on the floor about 0.5 meters in front of the tape that is marked at 0 meters.  Start the car and allow it to move toward the 0 meter mark.

- When the front of the car reaches the 0 meter mark, start your stopwatch.  Then, stop the stopwatch when the front of the car reaches the 1 meter mark.  Record the time in the table below.

- Repeat this procedure for 2 more trials.

- Calculate the average time and record in the table.

- Calculate the average speed using the formula given in the background and record in the table.

- Repeat the steps above, but this time allow the car to move from the 0 meter mark to the 200 cm mark.  Do this for three trials.  Then, do the same thing and allow the car to move from the 0 centimeter mark to the 300 centimeter mark and do this for three trials.  Record the Toy Car name above the data table.

Toy Car #1 Name = ____________________________________________________

| Distance traveled (cm) | Time Trial 1 (s) | Time Trial 2 (s) | Time Trial 3 (s) | Average Time (s) | Average Speed (cm/s) |
| --- | --- | --- | --- | --- | --- |
| 100 |  |  |  |  |  |
| 200 |  |  |  |  |  |
| 300 |  |  |  |  |  |

Questions:

- Was there a significant difference in the speed of the car while it traveled 100 cm versus 300 cm?  Explain why.

- What happens to the time of travel of the car if the distance that the car moves increases?

- Why did the lab directions require you to start the motion 50 cm in front of the 0.0 cm tape mark?

- What is the reason for re-running the experiment with multiple trials?  Why not let the car run one time and record the time?

- Repeat the lab with a different Toy Car.  Record the name of the Toy Car above the Data Table.

Toy Car #2 name = _______________________________________________

| Distance traveled (cm) | Time Trial 1 (s) | Time Trial 2 (s) | Time Trial 3 (s) | Average Time (s) | Average Speed (cm/s) |
| --- | --- | --- | --- | --- | --- |
| 100 |  |  |  |  |  |
| 200 |  |  |  |  |  |
| 300 |  |  |  |  |  |

- Repeat the lab with a different Toy Car.  Record the name of the Toy Car above the Data Table.

Toy Car #3 name = _______________________________________________

| Distance traveled (m) | Time Trial 1 (s) | Time Trial 2 (s) | Time Trial 3 (s) | Average Time (s) | Average Speed (cm/s) |
| --- | --- | --- | --- | --- | --- |
| 100 |  |  |  |  |  |
| 200 |  |  |  |  |  |
| 300 |  |  |  |  |  |

Graph the Data for all three Toy Cars on the provided Graph paper.  Be sure to include the following in the graph:

- Title the graph: “Speed of Toy Cars”

- Label the x and y-axes with variable names and units

- Scale the graph with appropriate number values

- Plot the data and circle the data points

- Provide a legend for each Toy Car

- Draw the best fit line or curve.

Describe the type of motion shown for each car on the graph.  Remember on a Position Graph the slope = the speed.  Straight line = constant speed, steeper slope = greater speed, and o slope = no speed.

Car #1  motion is _______________________________________________________

Car #2 motion is _______________________________________________________

Car #3 motion is _______________________________________________________

Which car had the greatest speed? ________ How does the graph indicate this? _______________________